​

🐢
Turtle Architecture Specification
Tom Riley
2026-01-06
Version 0.1.1
# Architecture Philosophy
The following are the guiding principles and philosophy that went into the design of the architecture:
- The architecture should be implementable with very simple hardware, e.g. with discrete logic gates
- Where trade-offs between hardware complexity and speed exist, prioritize minimizing hardware complexity
- Instructions should be simple, uniform, and complete in a single cycle where possible
- The design should be modular with a clear data path
# Properties
Table 1 Summary of CPU Properties
Property	Property Abbr.	Property Value
Data width	DATA_W	8 bits
Data Address width	D_ADDR_W	12 bits
Instruction width	INST_W	16 bits
Instruction Address width	I_ADDR_W	12 bits
Number of general-purpose registers	NUM_GPR	8

# Registers
Table 2 Register list
Register Abbr.	Width	Register Name	Description
PC	I_ADDR_W	Program Counter	Address of current instruction
ACC	DATA_W	Accumulator	Special register which is the implicit operand and result of most ALU, register, and memory instructions
DMAR	D_ADDR_W	Data Memory Address Register	Memory address for accesses / (DBAR << DATA_W) | DOFF
DBAR	D_ADDR_W - DATA_W	Data Memory Base Address Register	Upper part of memory address for accesses / DMAR[D_ADDR_W-1:DATA_W]
DOFF	DATA_W	Data Memory Address Offset Register	Lower part of memory address for accesses / DMAR[DATA_W-1:0]
IMAR	I_ADDR_W	Instruction Memory Address Register	Memory address for accesses / (IBAR << DATA_W) | IOFF
IBAR	I_ADDR_W - DATA_W	Instruction Memory Base Address Register	Upper part of memory address for accesses / IMAR[I_ADDR_W-1:DATA_W]
IOFF	DATA_W	Instruction Memory Address Offset Register	Lower part of memory address for accesses / IMAR[DATA_W-1:0]
R0...Rn	DATA_W	0…NUM_GPR-1 / General purpose Register	General purpose registers
STATUS	DATA_W	Status Register	Encodes the following statuses based on the Accumulator: / [0] zero (Z) / non-zero (NZ) / [1] positive (P) / negative (N) / [2] carry-set (CS) / carry-cleared (CC) / [3] overflow-set (OS) / overflow-cleared (OC) Note: The carry flag (CS/CC) indicates there was an unsigned overflow in ADD instructions, or that there was not a carry required in SUB instruction (like ARM but inverse to x86)

# Instructions
## Arithmetic / Logic (ALU)
Table 3 Register / Accumulator Arithmetic Instructions
OP CODE	Format	Description
ADD	ADD REG	Add register and Accumulator, place result in Accumulator
SUB	SUB REG	Subtract register from Accumulator, place result in Accumulator
AND	AND REG	AND register and Accumulator, place result in Accumulator
OR	OR REG	OR register and Accumulator, place result in Accumulator
XOR	XOR REG	XOR register and Accumulator, place result in Accumulator
INV	INV	Invert Accumulator, place result in Accumulator

Table 4 Immediate / Accumulator Arithmetic Instructions
OP CODE	Format	Description
ADDI	ADDI Imm	Add immediate value and Accumulator, place result in Accumulator
SUBI	SUBI Imm	Subtract immediate value from Accumulator, place result in Accumulator
ANDI	ANDI Imm	AND immediate value and Accumulator, place result in Accumulator
ORI	ORI Imm	OR immediate value and Accumulator, place result in Accumulator
XORI	XORI Imm	XOR immediate value and Accumulator, place result in Accumulator

## Register Instructions
Table 5 Register Instructions
OP CODE	Format	Description
SET	SET Imm	Set immediate value into Accumulator
PUT	PUT REG	Put Accumulator value into register
GET	GET REG	Get register value, place into Accumulator

## Memory
Table 6 Memory Instructions
OP CODE	Format	Description
LOAD	LOAD	Load value at Data Memory Address Register into Accumulator
STORE	STORE	Store Accumulator value into memory at Data Memory Address Register

## Special Instructions
The following instructions are special instructions which are aliases of existing instructions. They do not have independent encodings, and implementations may not have special hardware to implement them.
Table 7 Special Instructions
OP CODE	Alias	Description
NOP	ADDI 0	Intention is an instruction that does not change system state, but does move PC forward at the end
HALT	JMPI 0	Intention is an instruction that halts system progress, including PC

	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
Conditional Branch Instruction Format	address_immediate												branch_condition			1
Jump Immediate Format	address_immediate												op			0
Data Immediate Format	data_immediate								function				op			0
Register Format	reserved_12_15				register				function				op			0
No operand Format	reserved_12_15				reserved_8_11				function				op			0
ADD	reserved_12_15				register				ADD				ARITH_LOGIC			0
SUB	reserved_12_15				register				SUB				ARITH_LOGIC			0
AND	reserved_12_15				register				AND				ARITH_LOGIC			0
OR	reserved_12_15				register				OR				ARITH_LOGIC			0
XOR	reserved_12_15				register				XOR				ARITH_LOGIC			0
INV	reserved_12_15				reserved_8_11				INVERT				ARITH_LOGIC			0
ADDI	data_immediate								ADD				ARITH_LOGIC_IMM			0
SUBI	data_immediate								SUB				ARITH_LOGIC_IMM			0
ANDI	data_immediate								AND				ARITH_LOGIC_IMM			0
ORI	data_immediate								OR				ARITH_LOGIC_IMM			0
XORI	data_immediate								XOR				ARITH_LOGIC_IMM			0
SET	data_immediate								SET				REG_MEMORY			0
PUT	reserved_12_15				register				PUT				REG_MEMORY			0
GET	reserved_12_15				register				GET				REG_MEMORY			0
LOAD	reserved_12_15				reserved_8_11				LOAD				REG_MEMORY			0
STORE	reserved_12_15				reserved_8_11				STORE				REG_MEMORY			0
JMPI	address_immediate												JUMP_IMM			0
JMPR	reserved_12_15				reserved_8_11				RELATIVE				JUMP			0
JMP	reserved_12_15				reserved_8_11				ABSOLUTE				JUMP			0
BZ	address_immediate												ZERO			1
BNZ	address_immediate												NOT_ZERO			2
BP	address_immediate												POSITIVE			3
BN	address_immediate												NEGATIVE			4
BCS	address_immediate												CARRY_SET			5
BCC	address_immediate												CARRY_CLEARED			6
BOS	address_immediate												OVERFLOW_SET			7
BOC	address_immediate												OVERFLOW_CLEARED			8

# Encodings
Table 8 Opcode Format Encodings
OP Format	Encoding (binary)
ARITH_LOGIC_IMM	000
ARITH_LOGIC	001
REG_MEMORY	010
JUMP_IMM	100
JUMP_REG	111

Table 9 Arithmetic / Logic Function Encodings
Function	Encoding (binary)
ADD	0000
SUB	0001
AND	0010
OR	0100
XOR	0101
INV	0111

Table 10 Register / Memory Function Encodings
Function	Encoding (binary)
LOAD	0000
STORE	0001
GET	0010
PUT	0011
SET	0100

Table 11 Jump Function Encodings
Function	Encoding (binary)
RELATIVE	0000
ABSOLUTE	0001

Table 12 Branch Condition Encodings
Branch Condition	Encoding (binary)
ZERO	000
NOT_ZERO	001
POSITIVE	010
NEGATIVE	011
CARRY_SET	100
CARRY_CLEARED	101
OVERFLOW_SET	110
OVERFLOW_CLEARED	111

Table 13 Register Encodings
Branch Condition	Encoding (binary)
R0..R7	0000..0111
ACC	1000
DBAR	1001
DOFF	1010
IBAR	1101
IOFF	1110
STATUS	1111