🐢
Turtle Microarchitecture and Detailed Design Specification
Tom Riley
2026-01-06
Version 0.2.1

Turtle CPU Architecture
# Overview
The Turtle CPU is an 8-bit Microcomputer CPU designed to be made from discrete 74-series TTL logic chips. The name “Turtle” comes for “TTL” and from the design philosophy of being reliable—and slow. The design is an implementation of the Turtle CPU Architecture Error: Reference source not found. The following figures show a high-level overview of the blocks in the design, as well as the detailed module connections.

Figure 1 Turtle CPU Overview Block Diagram

Figure 2 Turtle CPU Detailed Top Level Diagram
# Modules
## Clock and Reset Generator
Table 1: Clock and Reset Generator Module Ports
Port Name	Direction	Width	Description
reset_btn	Input	1	Reset button input (active high), simulating an external reset button
manual_clk_sw	Input	1	Manual clock switch to select between automatic and manual clock
pulse_clk_btn	Input	1	Manual clock pulse button, simulating an external clock step button
clk	Output	1	System clock output, free running based on parameter value
reset_n	Output	1	Active-low reset signal

## Arithmetic Logic Unit (ALU)
Table 2: Arithmetic Logic Unit (ALU) Module Ports
Port Name	Direction	Width	Description
operand_a	Input	DATA_W	First operand input
operand_b	Input	DATA_W	Second operand input
alu_func	Input	3	ALU function selector (ADD, SUB, AND, OR, XOR, INV) (Encoding defined in )
output_enable	Input	1	Enable signal for ALU result output tri-state. When low, alu_result is Hi-Z to allow the bus to be driven elsewhere
alu_result	Output	DATA_W	Tri-state ALU result output
zero_flag	Output	1	Zero flag (result == 0)
positive_flag	Output	1	Positive flag (MSB of result == 0)
carry_flag	Output	1	Carry flag (for ADD/SUB operations)
signed_overflow	Output	1	Signed overflow flag (for ADD/SUB operations)

## Instruction Decoder
Table 3: Instruction Decoder Module Ports
Port Name	Direction	Width	Description
instruction	Input	INST_W	16-bit instruction word
address_immediate	Output	I_ADDR_W	Immediate address for branch/jump instructions
acc_immediate	Output	DATA_W	Tri-state immediate value for accumulator
alu_operand_b_immediate	Output	DATA_W	Tri-state immediate value for ALU operand B
acc_write_enable	Output	1	Enable signal for accumulator write
write_put_acc	Output	1	Enable signal for PUT operation (ACC → register)
read_get_acc	Output	1	Enable signal for GET operation (register → ACC)
reg_addr	Output	4	Register address for register file access
read_data_output_enable	Output	1	Tri-state enable signal for register read data output
status_write_enable	Output	1	Enable signal for status register write
data_memory_write_enable	Output	1	Enable signal for data memory write
data_memory_output_enable	Output	1	Tri-state enable signal for data memory read
jump_branch_select	Output	1	Enable signal for jump/branch operations
immediate_address_select	Output	1	Select immediate address for branch
unconditional_branch	Output	1	Flag for unconditional branch
pc_relative	Output	1	Whether to jump relative to PC (1) or to an absolute address (0)
branch_condition	Output	3	Branch condition selector
alu_output_enable	Output	1	Enable signal for ALU output
alu_function	Output	3	ALU function selector (Encoding defined in [1])

## Program Counter
Table 4: Program Counter Module Ports
Port Name	Direction	Width	Description
clk	Input	1	System clock
rst_n	Input	1	Active-low reset signal
imar	Input	I_ADDR_W	Instruction Memory Address Register
address_immediate	Input	I_ADDR_W	Immediate address for branch instructions
jump_branch_select	Input	1	Enable signal for jump/branch instructions
immediate_select	Input	1	Select immediate address for branch
pc_relative	Input	1	Whether to jump relative to PC (1) or to an absolute address (0)
unconditional_branch	Input	1	Flag for unconditional branches
status_register	Input	DATA_W	Status register containing flags
branch_condition	Input	3	Branch condition to evaluate
pc	Output	I_ADDR_W	Program Counter output

## Register File
Table 5: Register File Module Ports
Port Name	Direction	Width	Description
clk	Input	1	System clock
reset_n	Input	1	Active-low reset signal
acc_out	Output	DATA_W	Accumulator output (always available)
acc_in	Input	DATA_W	Accumulator input from tristate bus
acc_write_enable	Input	1	Write enable for accumulator
read_get_to_acc	Input	1	Enable for internal tristate from read_data to acc_in
write_put_acc	Input	1	Enable for internal write from ACC to reg[reg_addr]
reg_addr	Input	4	Register address for read/write operations
read_data_output_enable	Input	1	Enable for read data tristate output
read_data	Output	DATA_W	Tri-state output for read data
status_write_enable	Input	1	Enable for status register write
zero_flag	Input	1	Zero flag from ALU
negative_flag	Input	1	Negative flag from ALU
carry_flag	Input	1	Carry flag from ALU
overflow_flag	Input	1	Overflow flag from ALU
dmar	Output	D_ADDR_W	Data Memory Address Register
imar	Output	I_ADDR_W	Instruction Memory Address Register

## Instruction Memory
Table 6: Instruction Memory Module Ports
Port Name	Direction	Width	Description
addr	Input	I_ADDR_W	Address input for instruction fetch
instruction	Output	INST_W	16-bit instruction output

## Data Memory
Table 7: Data Memory Module Ports
Port Name	Direction	Width	Description
data_addr	Input	D_ADDR_W	Address input for data memory access
write_data	Input	DATA_W	Data input for memory write operations
write_enable	Input	1	Enable signal for memory write
output_enable	Input	1	Enable signal for memory read output
read_data	Output	DATA_W	Tri-state data output for memory rea

# Interconnection (Headers)

Figure 3 Interconnection Between Different Modules